## Slide 1
VNM PEDAL LITE
Quick Guide
Content
5
6
1. VNM Throttle
2. VNM Brake
3. VNM Clutch
4. VNM Controller Box
5. USB Cable
6. Allen key set & Mounting screws
7. Red & Yellow springs
Connection
1
2
4
3
On the left side of the VNM Controller Box is:
1. Handbrake 3. Brake
2. Throttle 4. Clutch
Plug in the GX12 ports for signal connection.
On the right side of the VNM Controller Box is:
5. Switch DFU/Game Mode
Slide left side to select DFU Mode or right side to select Game Mode.
6. Plug in USB cable to connect to PC.
Adjust Pedal
7
1. Adjust the height of the Pedal face
3. Adjust the Pedal Force
In addition, you can also change the force by adjusting the position of the screw here
2. Adjust the Pedal tilt angle
Here we give 6 options so you can change the angle of the pedal to your liking.
Remove the 2 hex bolts on the sides, then choose the angle that suits you and tighten them with the hex bolts.
5
6
1
2
3
4
5
6
Loosen the 4 the hex bolts on the sides behind the pedal face, choose a suitable pedal height, then tighten.
1
2
3
4
Adjust the spring preload so that the pedal force is right for your foot

## Slide 2
Step 1: Remove the elastomer stack
Step 2: Choose a suitable combination of springs and elastomers
Option 1: Red, Blu, Yellow spring + 2 elastomers
Option 2: Steel spring + 2 elastomers
Option 3: 2 springs + 1 elastomer
3 combinations are recommended, but feel free to mix and match to find the perfect combo for you.
Step 3: Re-install the elastomer stack
4. Adjust the Pedal Journeys
Loosen the 2 hex bolts on the sides, adjust 2 blue bumpstops to change pedal stroke
5. Exchange Spring & Elastomer
Blue Bumpstop 1:
Move blue bombstop to change pedal stroke limit.
Blue Bumpstop 2:
Adjust the inclination of the pedal face (pedal stroke start point)
Adjusting the Blue Bumpstop 1
Step 1: Remove spring assembly.
Step 2: Loosen the hex bolts 1 & 2 on the sides then choose the location of the blue bumpstop that works for you and tighten the hex bolts 2 you just loosened.
Step 3: Move the locating pin to fix the hex bolt 2 then tighten the hex bolt 1 (with VNM Throttle and VNM Clutch).
Step 4: Reinstall the spring assembly.
Remove bolts then remove spring assembly
min
max
min
max
1
2
1
2
Reinstall the stack and adjust the preload to your liking.

## Slide 3
Mounting Drawing Throttle
Mounting Drawing Brake
Mounting Drawing Clutch
Mounting Drawing Controller Box