## Slide 1
Content
Step 1: Remove the spring
Step 2: Replace the spring assembly with the damper cylinder
Step 3: Install the damper
Damper
3D printed spacer
M5x4 flat-headed grub screw
M5x4 plastic-headed grub screw
Step 1.1: Remove the grub screw
Step 1.3: Remove the spring assembly from the throttle unit
Install the included spring to the damper to replace the basic spring assembly.
Step 1.2: Loosen the spring preload
Twist the damper into the large threaded hole
Rotate the damper bracket so that it faces upwards
Step 5: Adjust the damper
Push the 3D printed adjuster into the cylinder and twist until it touches the damper bracket. Tighten using the grub screw and remove the adjuster.
Step 4: Fix the damper rod’s end to the pedal arm
Insert the damper rod’s end into the hole and tighten with the grub screw
Damper Springs
Pads Springs
Adjust Springs